## Slide 1: MAPS AND VISUALIZATIONS

## Slide 2
Cartography: The art, science, and techniques of making maps or charts.
Two types of GIS output:
  Maps
    Digital or analog (hard-copy) output from a GIS that shows geographic information using well-established cartographic conventions.
  Visualizations
    An interface to digitally display, analyze, edit, and query geographic information.

## Slide 3: Two Basic Map Types
Reference Maps:

## Slide 4: Two Basic Map Types
Thematic Maps:

## Slide 5
Maps are good for:
  Storage of Spatial Data
  Communication of Spatial Information
  Creating and or Reinforcing a Particular Message
Limitations:
  Can Miscommunicate (accidentally or on purpose)
  Single realization of a spatial process
  Complex rules, symbology, conventions

## Slide 6: Some Constraints Inherent in Paper Maps
Fixed Scale
Fixed Extent
Static View
2-dimensional

## Slide 8: Principles of Map Design
Primary Goals:
  Share information
  Highlight patterns and processes
  Illustrate Results
Secondary Objective:
  Create a pleasing and interesting picture

## Slide 9: 7 Controls of the Map Design Process
Purpose
Reality
Available Data
Map Scale
Audience
Conditions of Use
Technical Limits

## Slide 10: Map Composition
Map Elements
  Map Body
  Inset (Overview) Map
  Title
  Legend
  Scale
  Direction Indicator
  Map Metadata
Layout should have good visual balance

## Slide 11
Title
Legend
Projection
Grid
Data Source
Inset map
Map Body
Author
North Arrow
Scale

## Slide 12: Map Symbolization
Data is Classified and Represented using graphic symbols and colors that conform to well-defined conventions.

## Slide 13: Attribute Representation
Symbols representing attributes are classified in various ways to communicate different types of information
Four basic classification schemes:
  Natural Breaks (Jenks)
  Quantile Breaks
  Equal Interval Breaks
  Standard Deviation Classifications

## Slide 14: Natural Breaks (Jenks)
Class breaks conform to gaps in data distribution. Minimizes variation within classes, and maximizes variation between classes.

## Slide 15: Quantile
Equal number of observations within each class. Class intervals can be significantly different in size with this classification.

## Slide 16: Equal Interval
Equal distance between class breaks. The range of value that the class represents is the same for all classes.

## Slide 17: Standard Deviation
Class breaks based on a distance of standard deviation from the mean. Useful if data is distributed along a normal curve.